Division 12- Furnishings

Section 12492- Vertical Blinds

PART 1 General

1.01 SCOPE

A.  Supplier: Furnish and install manually operated, Vertical Blinds, including operating mechanism and mounting hardware according to Architectural Window Treatment Schedule.

B. RELATED WORK SPECIFIED IN OTHER SECTIONS

1.) Section 06100: Rough Carpentry

2.) Section 08520 Aluminum Windows

1.02 REFERENCES

A. FLAME RESISTANT MATERIALS SHALL PASS OR EXCEED ONE OR MORE OF THE FOLLOWING TESTS:

1.) National Fire Protection Association (NFPA) 701 (small scale for horizontal applications)

2.) California Administrative Code Title 19

1.03 SUBMITTALS

A. Submit under provisions of Section 01 3000

B. PRODUCT DATA: Submit Manufacturer's literature  and installation instructions indicating materials, finishes construction and installation instructions, verifying product meets requirements specified. Include manufacturers recommendations for maintenance and cleaning.

C. SAMPLE: Responsible Dealer or agent to supply two samples of louver for color choice. If needed, supply one sample  of each type of blind specified in this contract for approval. Supplied units shall be furnished complete with all requirements, mounting and associated hardware and instructions. Supplied unit to be used later as installed product.

1.04 QUALITY ASSURANCE

A. SUPPLIER: Manufacturer, subsidiary or licensed agent shall be approved to supplied products specified and to honor claims against product presented in accordance with warranty.

B. INSTALLER: Installer or agent shall be qualified to install specified products by prior experience, demonstrated performance and acceptance of requirements of manufacturer, subsidiary, or licensed agent. Installer is responsible for acceptable installation.

C. UNIFORMITY: Provide vertical blinds of only one manufacturer for entire project.

1.05 DELIVERY, STORAGE AND HANDLING:

A. Product shall be delivered to site in manufacturers original packaging.

B. Product shall be handled and stored to prevent damage to materials, finishes and operating mechanisms.

1.06 JOB CONDITIONS

A. Prior to vertical blind installation, building shall be enclosed.

B. Interior temperature shall be maintained between 60 degrees and 90 degrees F during and after installation. Relative humidity shall not exceed 80%. Wet work shall be complete and dry.

1.07 WARRANTY

Lifetime Limited Warranty: Specific product warranties available from manufacturer or authorized dealer. This warranty does not include any conditions or damages resulting from accidents, alterations, misuse, abuse, excessive humidity, misapplication, exposure to the elements, fire, flood, or other acts of God, improper maintenance or failure to follow use, care or installation instructions.

Part 2 -Products

2.01 ACCEPTABLE MANUFACTURER

A.  Lafayette Interior Fashions/3000 Klondike Road/ West Lafayette Indiana 47996. Telephone: 765-464-2500/ Fax: 413-480-4459 Email: quotes@lafvb.com

B .Submit Product substitutions for approval under provisions set forth in Section 01600. Manufacturer must be approved 10 days prior to close of bid.

2.02  Vertical Blind

A. PRODUCT: Lafayette Interior Fashions Discoveries Vertical Blind

MATERIAL

1. LOUVERS: 3.5" wide ± 1/16th inch X .032 maximum thickness curved thick louver with overlap of not less than 3/8" and stacking 7/32" apart. Finish to be selected by architect from manufacturers standard color offering.

2. CHANNEL: Standard Decomatic channel measuring 1.5" X 1"  constructed of painted anodized aluminum.  Fitted with extruded aluminum Decomatic wand draw or Decomatic cord draw, engineered thermal plastic carrier trucks, end caps and components required for specified performance.

3. CARRIER TRUCKS:   Engineered thermal plastic 7/16" thick and 1-5/8" wide with wheels and worm and spur gears to ensure rotation with perfect alignment and synchronization. Provide solid molded engineered thermal plastic asymmetrical carrier stems for easy louver installation and removal. Wheel-less lead carrier moves along elongated bearing surface.

4. SPACER LINKS: Provide stainless steel 1/4" X .008 space links to space and stabilize carrier trucks.

5. ROTATION: Provide Standard #6 nickel-plated brass tilt chain. Chain to provide 180 degree direct rotation by activating tilt gear within end cap assembly, then in turn actuating heavy duty extruded aluminum tilt rod and worm and gears in carrier trucks. Chain must be able to be located on either side of individual blind unit.

6. TRAVERSING:  Stretch resistant, non-fraying and lint free lock nit polyester cord to provide traversing capabilities for side, center and off center draws.

7.MOUNTING HARDWARE: Provide manufacturer's standard L-bracket with clip on outside mounts and clip only for inside mounts for required support.

8. ADDITIONAL AVAILABLE OPTIONS: Wand control, valances,  controls available on right or left side, cut outs to avoid obstructions,

2.03 FABRICATION

A. Blind measurements shall be accurate to within ± 1/8" or as recommended by manufacturer.

2.04 FINISHES

A.  FINISH SELECTION to be from manufacturers standard selection of patterns and colors

Part 3-Execution

3.01 INSPECTION

A. Subcontractor shall be responsible for inspection on site, approval of mounting surfaces, installation conditions and field measurement for this work.

B. Other interacting trades shall receive information regarding dimensions of vertical blinds, assembly and installation methods from subcontractor upon request

.

3.02 INSTALLATION

A. Install vertical blinds in accordance with approved submittals and manufacturers written instructions. Install in proper relationship to adjacent construction.

B. Installation shall comply with manufacturers specifications, standards and procedures as detailed in submittals.

C. Adequate clearance shall be provided to permit unencumbered operation of vertical  blind and hardware.

3.03 CLEANING AND PROTECTION

A. Clean installed products in accordance with manufacturers recommendations. Clean finished installation of dirt and grime. Leave work area clean and free of debris.

B. Protect installed products until completion of project.

3.04 SCHEDULE

A. Exterior Windows

B. Interior Finishes

End of Section 12492