Division 12- Furnishings

Section 12492- DUAL TRANSITIONAL SHADES

PART 1 General

1.01 SCOPE

A.  Supplier: Furnish and install dual light filtering and black out Transitional Shades, manually operated,  vertical roll up, according to Architectural Window Shade Schedule.

B. RELATED WORK SPECIFIED IN OTHER SECTIONS

1.) Section 06100: Rough Carpentry

2.) Section 08520 Aluminum Windows

1.02 REFERENCES

A. Flame resistant materials shall pass or exceed at least one of the following tests:

1.) National Fire Protection Association, N.F.P.A. 701 (small scale)

2.) California Title 19, Section 1237

1.03 SUBMITTALS

A. Submit under provisions of Section 01 3000

B. PRODUCT DATA: Submit Manufacturer's literature  and installation instructions indicating materials, finishes, construction and installation instructions, verifying product meets requirements specified. Include manufacturers recommendations for maintenance and cleaning.

C. SAMPLE: Responsible dealer or agent to supply sample of fabric for color choice. If needed, supply one sample of each type of each Transitional Shade specified in this contract for approval. Supplied units shall be furnished complete with all requirements, mounting and associated hardware and instructions. Supplied sample can be used as a manufactured product for installation on the project.

1.04 QUALITY ASSURANCE

A. SUPPLIER: Manufacturer's dealer, subsidiary or authorized agent shall be approved to supply products specified and to honor claims against product presented in accordance with warranty.

B. INSTALLER: Installer or agent shall be qualified to install specified products by prior experience, demonstrated performance and acceptance of requirements of manufacturer, subsidiary, or authorized agent. Installer is responsible for acceptable installation.

C. UNIFORMITY: Provide Transitional Shades of only one manufacturer with proven experience in manufacturing product for entire project.

1.05 DELIVERY, STORAGE AND HANDLING:

A. Product shall be delivered to site in manufacturers original packaging.

B. Product shall be handled and stored to prevent damage to materials, finishes and operating mechanisms.

1.06 JOB CONDITIONS

A. Prior to Transitional Shade installation, building shall be enclosed with windows installed complete with framing. Interior finishes should be dry and near completion.

B. Interior temperature shall be maintained between 60 degrees and 90 degrees F during and after installation. Relative humidity shall not exceed 80%. Wet work shall be complete and dry.

1.07 WARRANTY

Lifetime Limited Warranty. Specific product warranties available from manufacturer or authorized dealer.  This warranty does NOT include any conditions or damages resulting from accidents, alterations, misuse, excessive humidity, misapplication, exposure to the elements, fire, flood or other acts of God, improper maintenance, or failure to follow use, care or installation instructions.

Part 2 -Products

2.01 ACCEPTABLE MANUFACTURER

A.  Lafayette Interior Fashions/3000 Klondike Road/ P.O. 2838/West Lafayette Indiana 47996. Telephone: 765-464-2500/ Fax: 413-480-4459 Email: quotes@lafvb.com

B. Submit Product Substitutions for approval under provisions set forth in Section 01600. Manufacturer must be approved 10 days prior to close of bid.

2.02 COMMERCIAL TRANSITIONAL SHADE

A. PRODUCT: ALLURE DUAL TRANSITIONAL SHADE

B. MATERIALS

1. FABRIC:

a. Light filtering fabric to be one single continuous polyester fabric connected to a roller tube and looped through an aluminum bottom rail.  Fabric is connected to the back of the head rail. Choice of  fabric to be selected by Architect from manufacturer's available standard  materials.

b. Room darkening shade to be flame retardant treated polyester and acrylic blend selected from manufacturer's available standard fire rated fabrics. Fabric to be positively attached using double sided adhesive tape to secure shade fabric to roller.

2. HEAD AND BOTTOM RAIL: Standard Aluminum Head Rail constructed of aluminum alloy conceals shading when fully raised. Internally fit with components required for specified performance and designed for smooth, quiet, trouble-free operation. Concealed bottom rail for light filtering shade  constructed of aluminum alloy. Available in any one of  five standard polyester-based paint finishes of 03 black, 09 Vanilla, 11 White, 38 Bronze, or 90 Brushed Nickel  to coordinate with fabric.   End caps to be color coordinated with hardware.

Room darkening shade bottom rail to be constructed of metal, fabric wrapped with hem. Optional aluminum weight bar, sealed or sewn into a pocket, depending on fabric choice. Best practice to be determined by manufacturer.

3.) LIFTING/ROTATION MECHANISM: Clutch to be Fiberglass reinforced Resin PBT spring assist rotary clutch system will raise and lower shade when activated. Continuous beaded chain will activate gear in clutch for raising and lowering shade. Chain must be able to be located on either side of shade. Standard low profile cassette to be used where possible. Larger cassette size to be based on shade size and material choice. Cassette size to be determined by manufacturer based on window size and fabric choice

4.) MOUNTING HARDWARE: Manufacturer's standard steel  brackets, provided in any of five finishes. Manufacturer  to coordinate from  03 Black, 09 Vanilla, 11 White, 38 Bronze or 90 Zinc Plated to coordinate with head rail choice.

5.) ADDITIONAL AVAILABLE OPTIONS:  Optional fabric upgrades, motorization, optional cord lengths and hold down brackets.

2.03 FABRICATION

A. Transitional Shade  measurements shall be accurate to within ± 1/8" or as recommended in writing from manufacturer.

2.04 FINISHES

A.  Fabric finish to be polyester for ease of cleaning.  Light filtering fabric choices to have various degrees of opacities and translucency depending on fabric choice. Standard fabric choices are Mystic, Entice and Appeal. See Additional Available options for additional fabric choices. Selection to be made prior to specification publication.

Part 3-Execution

3.01 INSPECTION

A. Subcontractor shall be responsible for inspection on site, approval of mounting surfaces, installation conditions and field measurement for his work.

B. Other interacting trades shall receive information regarding dual roller shade dimensions, assembly and installation methods from subcontractor upon request.

3.02 INSTALLATION

A. Install systems in accordance with approved submittals and manufacturer’s written instructions.  Install in proper relationship to adjacent construction.

B. Test for operation as recommended by manufacturer.  Repair or replace units until satisfactory results are obtained.

C. Installation shall comply with manufacturers specifications, standards and procedures   as detailed in submittals.

D. Adequate clearance shall be provided to permit unencumbered operation of shade and hardware.

3.03 CLEANING AND PROTECTION

A.  Clean installed products in accordance with manufacturer’s recommendations. Touch-up, repair or replace damaged products before Substantial Completion.

B. Protect installed products until completion of project.

3.04 CONSTRUCTION SCHEDULE

A. Exterior Windows

B. Interior Finishes

End of Section 12492